## Slide 1
3D Object Detection with LiDAR-Camera Fusion
PointPillars + ResNet Architecture on KITTI-360 Dataset
FAORO LORENZO
December 8, 2025

## Slide 2
Project Overview & Objectives
Main Goal
Implement a multi-modal 3D object detection system that effectively combines LiDAR point clouds and camera images to increaese perception.
Target Objects
Cars
Pedestrians
Cyclists
Architecture
Hybrid deep learning architecture with PointPillars for LiDAR feature extraction and ResNet50 for camera image processing, integrated through a sophisticated fusion module.
Dataset
Utilize the KITTI-360 autonomous driving dataset, a comprehensive benchmark for urban scene understanding, to train and validate the model.
Training Environment
Conduct all training and development within Google Colab, utilizing its GPU acceleration capabilities to manage computational demands.

## Slide 3
KITTI-360 Dataset
Data Sources
LiDAR Point Clouds
Sensor: Velodyne HDL-64E laser scanner
Format: 1000 files in .bin format
Density: ~100,000 points per scan
Features: Each point includes (x, y, z, intensity) coordinates
Camera Images
Sensor: High-resolution RGB cameras
Format: 1000 images in .png format
Resolution: 376 x 1408 pixels
Synchronization: Temporally aligned with LiDAR scans
3D Annotations
Format: XML files
Content: 3D bounding boxes with position, size, and orientation,
Categories: Cars, pedestrians, cyclists, and ground elements
Key Features
Comprehensive urban scene understanding
Multimodal sensor data integration
Rich annotation for 3D object detection

## Slide 4
Data Preprocessing Pipeline
LiDAR Input
Binary .bin files with shape (N, 4) representing points as (x, y, z, intensity)
Camera Input
.png image files with shape (3, H, W) in RGB format
Point Cloud Processing
Subsampling: Max 50,000 points per scan
Zero-padding: Ensure consistent input size
Normalization: Preserves metric relationships
Image Processing
Resizing: To 256 x 512 pixels
Normalization: Pixel values to [0, 1]
Channel Ordering: (H, W, C) to (C, H, W)
Synchronization
Temporal Alignment: Ensures time correspondence
Matching: Based on file indices (e.g., 0000000000 to 0000001000)
Preprocessed Output
LiDAR:
(batch, 50000, 4)
Image:
(batch, 3, 256, 512)
MIDDLE-FUSION

## Slide 5
LiDAR Backbone - PointPillars
Input
(x, y, z, intensity)
PointPillars Architecture
Simplified for efficient feature extraction from point clouds
Stage 1
Point-wise Feature Extraction
MLP layers with BatchNorm & ReLU
Linear(4→64) → Linear(64→256)
Output: (batch, num_points, 256)
Stage 2
Global Feature Aggregation
Max pooling across all points
Captures global scene structure
Output: (batch, 256)
Stage 3
Bird's Eye View Generation
Expands global features to 2D grid
Creates pseudo-image representation
Output: (batch, 256, 64, 64)
Stage 4
2D CNN (convolution net.)Processing
Conv2d(256→512) + BN + ReLU
Conv2d(512→512) + BN + ReLU
Output: (batch, 512, 16, 16)
Final Output
(batch, 512, 16, 16)
Compact feature map for fusion with camera data
Batch Normalization + ReLU to get:
Stability
Faster training
One global vector for the feature of
the scene
From 3d to 2d
Process BEV with convolutional net.

## Slide 6
Image Backbone - ResNet50
Feature Extraction Pipeline
Input
(batch, 3, 256, 512) 3=RGB channels; 256 Height; 512 Width
Initial Convolution
7×7 convolution with step of 2p → (batch, 64, 128, 128)
Max Pooling
3×3 max pooling with step of 2 → (batch, 64, 64, 128)
Residual Blocks
Four layers extracting hierarchical features → (batch, 2048, 8, 16)
Channel Reduction
1×1 convolution → (batch, 512, 8, 16)
Feature Characteristics
Multi-scale hierarchical information
Rich semantic content
Perspective view representation
Texture, color, and appearance
Benefits
Strong initialization from ImageNet
Proven effective architecture
Robust feature extraction

## Slide 7
FusionModule with Attention
STEPS
GOAL: fuse data from lidar and camera in the best possible way which one makes the correct prediction?
STEP 1  ALLIGNMENT AND CALIBRATION of the two types of lidar and camera data
STEP 2 32x32 grid containing 512 lidar features (info) and 512 camera features
STEP 3  ATTENTION MECHANISM the network learns if trust to the camera or the lidar most
STEP 4  WEIGHTED FUSION application of different weight to the features
STEP 5  FINAL FUSION middle-fusion with attention

## Slide 8
Detection Head Architecture
Multi-Task Architecture
The detection head processes fused features to predict object classifications, 3D bounding box parameters, and object directions.
Classification Branch
Conv2d(256 → 3, )
Predicts class probabilities for Car, Pedestrian, Cyclist
3D Bounding Box Regression
Conv2d(256 → 7, )
Predicts 7 parameters: (x, y, z, l, w, h, θ)
(boxes position and orientation)
Direction Classification
Conv2d(256 → 2, )
Binary classification to disambiguate object orientation (if it’s front or back oriented)
Detection Process
Dense prediction over 32×32 grid in BEV Bird's Eye View space

## Slide 9
Training Strategy & Setup
Training Configuration
Framework & Hardware
PyTorch 2.0 on Google Colab GPU
Data Parameters
Batch Size: 4 | Training Samples: 800 | Validation Samples: 200 | Epochs: 13
Multi-Task Loss Function
Ltotal = Lclassification + Lregression + 0.2 × Ldirection
Binary Cross Entropy standard
3 classes (pedestrian…)
Smooth L1 regression bbox
σ=3.0
Cross Entropy
Weight: 0.2
Training Process
Learning Rate Schedule
Best Val Loss: 338
Best Train Loss: 226
Prediction vs reality
Underfitting?

## Slide 10
Training Results
The basic problems certainly lie in the simplicity of the model, the low number of samples analyzed, the underfitting
Detection of pedestrians and cyclists is very imprecise

## Slide 11
Conclusion
Key Achievements
Successfully implemented PointPillars + ResNet fusion architecture
Trained on KITTI-360 dataset with 1000 multi-modal samples
Achieved stable training with decreasing loss curves
Created an end-to-end pipeline from raw data to a trained model
Demonstrated the utility of LiDAR-Camera fusion for 3D detection
Current Limitations
Implementation parameter calibration
Overfitting - underfitting
Small dataset size (1000 samples)
The confidence in detecting pedestrians and bikes is lower than that of machines. During training there are few scenes of pedestrians and bikes, I think this is the main cause.
FRAME 200 OBJECTS: 11cars, 0 pedestrian, 0 cyclists 